## Slide 1
19/04/16
Data Communication Mini Project
<number>
IP address Assignment in a
Mobile Ad-hoc NETwork
By
Kavya Atmakuri - 14CO123
Sangeetha G S - 14CO141
Notes: <number>

## Slide 2
19/04/16
Data Communication Mini Project
<number>
MANET – (Mobile Ad hoc NETwork) is a continuously self-configuring, infrastructure-less network of mobile devices connected without wires.
MANET may be stand-alone or may be part of Internet.
It can change locations and configure itself on the fly.
They use wireless connections to connect to various networks.
Examples –
VANET (Vehicular Ad hoc NETwork) – used to keep track of trucking fleet or measure traffic conditions.
What is a Mobile Ad-hoc Network ?
Notes: Ad hoc in latin means ‘for this’
<number>

## Slide 3
19/04/16
Data Communication Mini Project
What is the problem?
MANET consists of mobile nodes
They cannot rely on DHCP for configuration since they are dynamic and distributed
Highly dynamic and autonomous topology.
Present Challenge – To build a MANET in which each device is equipped to maintain information required to route traffic.
The problem (in simple words) – Dynamic Allocation of IP addresses in MANETs
Current solutions are –
IPv6 stateless autoconfiguration mechanisms
Flooding the entire network to get unique IP Address

## Slide 4
19/04/16
Data Communication Mini Project
<number>
What solution have we implemented?
Binary Split – Distribute IP addresses among nodes so that each node can independently configure new nodes.
The Concept – BUDDY SYSTEM
  Every node that connects to the network has an IP block and an IP address assigned to itself.
  First node that gets connected to the network gets an IP address and an IP address block of maximum size.
  When more nodes, each node gets a ‘buddy’. The new node get an IP and an IP block by splitting the address block of its buddy.
  When a node leaves, the buddy or a nearby block gets the block of IP assigned to the leaving node. The leaving node’s IP is free and can be assigned to any new node.

## Slide 5
19/04/16
Data Communication Mini Project
<number>
Structure of a node
ID
IP_ADDRESS
IP_START_ADDRESS
IP_END_ADDRESS
….
….
….
ID IP_START IP_END
map[max][3]
available
valid
buddy
level
IP address block for each node

## Slide 6
19/04/16
Data Communication Mini Project
<number>
ID
IP_ADDRESS
IP_START_ADDRESS
IP_END_ADDRESS
….
….
….
ID IP_START IP_END
available
valid
buddy
level
OUR MANET
ID
IP_ADDRESS
IP_START_ADDRESS
IP_END_ADDRESS
….
….
….
ID IP_START IP_END
available
valid
buddy
level
N nodes connected wirelessly
…………………………….
GLOBALMAP ARRAY
….
….
….
NODE_ID IP_START IP_END
globalmap[max][3]

## Slide 7
19/04/16
Data Communication Mini Project
<number>
BINARY SPLIT APPROACH
START THE NETWORK
TO ADD A NODE
AddNode()
{
initialize()
update()
display()
}
TO REMOVE A NODE
RemoveNode(in Node_ID)
{
//assign the block to a buddy or nearby node
update()
display()
}

## Slide 8
19/04/16
Data Communication Mini Project
<number>
ADDING A NODE
InitializeNode()
{
//if node is the first node to connect to the network
//assign full address block to that node
//update global map
//else
//find a buddy
//see if buddy is available
//split the address block of buddy and assign
it to the new node.
//update the global map
}

## Slide 9
19/04/16
Data Communication Mini Project
<number>
REMOVING A NODE
RemoveNode(int NodeID)
{
//if node id is not valid
//invalid id – do nothing
//else
//invalidate the node
//look for the buddy or the nearest node
//assign the address block of the leaving node to the buddy/nearest node found.
//update the global map
}

## Slide 10
19/04/16
Data Communication Mini Project
<number>
OUTCOME
Buddy system is easily scalable
No infrastructural network => every node has equal work of assigning IP to the new node.
Overhead is less since the address block of each is well within the maximum address block size of the network.
CONCERNS :
  Security concern : Every node in this network trusts the other nodes.
  Malicious users can make nodes selectively assign wrong IP addresses which may lead to IP conflict which is difficult to resolve.

## Slide 11
19/04/16
Data Communication Mini Project
<number>
References
IP Address assignment in a mobile ad hoc network – Mansoor Mohsin and Ravi Prakash – MILCOM 2002
https://en.wikipedia.org/wiki/Mobile_ad_hoc_network

## Slide 12
19/04/16
Data Communication Mini Project
<number>
QUESTIONS?